## Slide 1: Wifi Hacking
Neko
Hacking wifi for fun and profit

## Slide 2: Abstraction
Layers

## Slide 3: Interpretation
Standards
Developer
Implementation

## Slide 4
What is it?
https://ieeexplore.ieee.org/browse/standards/get-program/page/series?id=68

## Slide 5: Radiation
Wifi
900 MHz
2.4 GHz
5 GHz
6 GHz

## Slide 6: 802.11/Wifi Generations
802.11 -> Wifi 0: 1997
802.11b -> Wifi 1: 1999
802.11a -> Wifi 2: 1999
802.11g -> Wifi 3: 2003
802.11n -> Wifi 4: 2009
802.11ac -> Wifi 5: 2013
802.11ax -> Wifi 6 (E for Extended!): 2019
802.11be -> Wifi 7: 2024
802.11bn -> Wifi 8: Unreleased

## Slide 7: Some Radio Stuffs
CSMA/CA
Multiplexing
FDM
OFDM
Multipath Propagation
MIMO

## Slide 8: CSMA/CA
Carrier Sense Multiple Access / Collision Avoidance
Is the channel busy?
May I please send? (RTS)
You are allowed to send (CTS)

## Slide 9: Multiplexing
One long signal in, multiple short signals out
Literally dividing transmission time by the number of distinct output signals

## Slide 10: FDM
Frequency Division Multiplexing
Total Band
Channel 1
Channel 2
Channel 3

## Slide 11: OFDM
Orthogonal Frequency Division Multiplexing
Total Band
Channel 1
Channel 3
Channel 5
Channel 2
Channel 4
Some overlapping is okay because of MATHS

## Slide 12: Multipath Propagation
The same signal may arrive multiple times and at different times

## Slide 13: MIMO
Multiple Input Multiple Output

## Slide 14: Generational Differences
Frequency bands (900 MHz, 2.4 GHz, 5 GHz, 6 GHz)
Modulation techniques
Channel widths (20 - 80 MHz)

## Slide 15: Frames
What are we sending anyway?

## Slide 16: Frame Size
16
16
0
or
32
0
or
16
48
0
or
16
48
48
48
32
0
to
18496
Bits

## Slide 17: Frame Control Field
2
2
4
1
1
1
1
1
1
1
1
00 unless 802.11ah/Wifi HaLow

## Slide 18: Frame Control Field
2
2
4
1
1
1
1
1
1
1
1
00 for management frame
01 for control frame
10 for data frame
11 for extension frame

## Slide 19: Subtypes of Management Frames
2
2
4
1
1
1
1
1
1
1
1
0000 association request
0001 association response
0010 reassociation request
0011 reassociation response
0100 probe request
0101 probe response
0110 timing advertisement
0111 reserved
1000 beacon
1001 ATIM
1010 disassociation
1011 authentication

## Slide 20: Subtypes of Management Frames Continued
2
2
4
1
1
1
1
1
1
1
1
1100 deauthentication
1101 action
1110 action no ack
1111 reserved

## Slide 21: Subtypes of Frame Types
2
2
4
1
1
1
1
1
1
1
1
Other frame type subtypes see:
https://en.wikipedia.org/wiki/802.11_frame_types#Types_and_subtypes

## Slide 22: To and From DS
2
2
4
1
1
1
1
1
1
1
1
Denotes if a frame is to or from a distributed system
This is how you can have multiple access points serving the same network

## Slide 23: More Fragments
2
2
4
1
1
1
1
1
1
1
1
Denotes that a frame is only part of a larger transmission and there are ‘more fragments’ on the way

## Slide 24: Retry
2
2
4
1
1
1
1
1
1
1
1
This is a retransmission of an earlier frame

## Slide 25: Power Management
2
2
4
1
1
1
1
1
1
1
1
Please hold, I’m going to nap
&
Okies, I’m awake, send the datas

## Slide 26: More Data
2
2
4
1
1
1
1
1
1
1
1
But wait, there’s more!

## Slide 27: Protected Frame
2
2
4
1
1
1
1
1
1
1
1
Is this a protected frame?

## Slide 28: Protected Frames
We can encrypt frames now???
YES! Optional for WPA2 and required for WPA3… except for…
Beacons
Probes
Authentication
Association
ATIM
Channel Switch Announcement as Broadcast

## Slide 29: High Throughput Control / Order
2
2
4
1
1
1
1
1
1
1
1
Indicates QoS or a high throughput control field

## Slide 30: Frame Addresses
To an Access Point
Address 1: BSSID
Address 2: Source
Address 3: Destination
Address 4: Not used

## Slide 31: Frame Addresses
From an Access point
Address 1: Destination
Address 2: BSSID
Address 3: Source
Address 4: Not used
Sniffing enabled BY DESIGN

## Slide 32: Frame Check Sequence
32 bit Cyclic Redundancy Check

## Slide 33: Look at our surroundings

## Slide 34: Let’s Listen
airodump-ng wlan1 -w lab —essid=wifilab-target-wep

## Slide 35: First Frame
Information we have
Addresses
OUIs
SSID

## Slide 36: WiGLE!
Real creeper hours

## Slide 37: Hidden Wifi Networks
Hidden text
Broadcast null byte for each character in ESSID.
Broadcast “” as ESSID
… Just wait for a probe from a client or an association

## Slide 38: Kismet

## Slide 39: Nzyme
Defender’s Kismet

## Slide 40: WEP Handshakes
May I please authenticate?
I CHALLENGE YOU!
*screams gibberish*
*encrypts the gibberish*
Oh, you got hands.
Nevermind, you can auth

## Slide 41: RC4 cola
Initialization vectors: 24 bits
WEP 40: 40 bit key + 24 bit IV = 64 bit key
WEP 104: 104 bit key + 24 bit IV = 128 bit key
IVs are transmitted in plaintext, you already know some of the key!

## Slide 42: WEP Cracking
Not enough traffic?
Try a replay attack with aireplay-ng —caffe-latte
Made possible by CRC

## Slide 43: Enter WPA
TKIP (Temporal Key Integrity Protocol)
  Dynamic 128-bit keys
  Still RC4 stream cipher
Sequence counter to counter replay attacks
MIC (Message Integrity Check)

## Slide 44: If WPA was so good, why isn’t there a WPA2?
CCMP (makes use of AES (which is a variant of Rijndael))
New Handshakes
Another 128-bit key
EAP and MSCHAPv2 vulns beyond scope
Aircrack dictionary attacks still work, so we have that going for us

## Slide 45: WPA2 Handshake
Here, have a random number (nonce)
Aww, thanks.
Here’s a random number for you too
*decides pairwise transient key*
Have some random data, on the house
Sweet, I can decrypt that and it’s a love note <3

## Slide 46: KRACK
Key Reinstallation Attack, just say no
Pretend to be the AP
Replay part 3 of the 4-way handshake
Reset incremental transmit packet & replay counter
…
Profit

## Slide 47: HOLE
Hole196
All clients have the same GTK (Group Transient Key)
So all clients can broadcast with that key
And pretend to be any other client, or the AP

## Slide 48: Well if WPA2 was so…
WPA3
TKIP was last years news
CCMP-128, still cool
GCMP? (AES-256 with SHA-384 for HMAC)
No more PSK (except with EAP), only SAE
KRACK still useful due to WPA2 - WPA3 transitional settings

## Slide 49: What is SAE?
Dragonfly / RFC7664
Uses “domain parameters” (PSK & MAC address)
Elliptic Curve Cryptography & Finite Field Cryptography
Forward Secrecy

## Slide 50: Frag Attacks
Frame Aggregation
Frame Fragmentation
  Mixed key attack (or even no key)
  Fragment cache attack
Some devices accept unencrypted frames… for the lolz
This is the bleeding edge and where my knowledge ends
Read https://www.fragattacks.com/

## Slide 51: Unless? WPS
EAP (Extensible Authentication Protocol)
8 digit pins

## Slide 52: Evil Twins
ESSIDs are changeable by nature
BSSIDs can be spoofed easily
    ‘ip link set dev wlan0 address c0:01:de:ad:be:ef’
                Can’t trick the computer? Try the user.

## Slide 53: Risks?
Get creative
Lots of sites load images over HTTP
XSS through JS in SVGs?
Insert shock image du jour?
You never know what’s plaintext
Thank you!